## Slide 1: FPGA based Audio Effects System
Presented by Dean Devereaux
Notes: Good morning
The project I have picked for final year is the FPGA based Audio effects system.
I chose this project as I have an interest in music and would have a lot of fun working with audio effects.
Audio effects really help shape music. Distortion would be associated with Rock music and a lot of 80’s music uses reverb and delay for vocals. It’s everywhere

## Slide 2: Aim of Project
Send audio through FPGA development board
Alter sent audio
Program Three Effects
  Delay
  Non-Linear Processing
  Spatial
Notes: The aim really is to program an FPGA to
Digitize input audio
Apply effect
Output altered analogy audio
I want to be able to program three effects onto the audio which would be echo, distortion and reverb
For this project I would like to test the end result with vocals, guitar and keyboard

## Slide 3: Hardware
Artix-7 FPGA
Pmod I2S
Notes: Artix-7 FPGA
Used on the basys3 development board.
Low cost and powered FPGA which can deal with advanced functionality.
Has a built in ADC which has a sampling rate of up to 1MS/s and can convert up to 12bits
Dynamic Reconfiguration Port(DRP) interface between ADC and FPGA
Vref: 1.25V-0V
DCLK: 8-250MHz
ADCCLK: 1-26MHz
Pmod I2S
Integrated Interchip Sound
6 Pin GPIO Interface
Convert up to 24bit
MCLK can run anywhere from 512 kHz to 50 MHz
LRLK(Sample Rate)
SCLK(Bit clock)

## Slide 4: Software
Vivado
Verilog
MATLAB
Notes: Xilinx design suite that deals with HDL Design.
Simulate and Program FPGA Board.
Programming the board with Verilog language.
MATLAB was used when testing the effects

## Slide 5: Block Diagram
Audio
Basys3
Pmod
Vivado
(PC)
Pmod JA
Pmod to
XADC
Altered Audio
Slide
Switches
Push
Buttons
Notes: Here is my block diagram for the project.
From the Basys3 I will be using:
  XADC
  x2 Pmod
  Slide Switches
  Push Buttons
  Four 7Seg Display
All external devices used are the Pmod and Audio Source
Here is my block diagram for the project.
From the Basys3 I will be using:
  XADC
  x2 Pmod
  Slide Switches
  Push Buttons
  Four 7Seg Display
  All external devices used are the Pmod I^2 S, Vivado and Audio Source

## Slide 6: Delay Effect
IIR Comb Filter
y
Notes: Difference equation
Involves feedback
Simulates endless reflections
Input fed back to itself and each time the gain attenuates the feedback.
Feedback data was saved in a shift register.
Called a comb filter because of the “comb” like frequency response due to notches
Resonator 0-20ms
Slapback 25ms-50ms
Echo > 50ms

## Slide 7: Delay Effect
FIR Comb Filter
y
Notes: Involves feedforward
Simulates single delay

## Slide 8: Spatial Effect
Schroeder Reverberator
Combination of IIR CF and Universal CF
Notes: Schroder reverberator is the original and primitive reverb method
To create this method, four comb filters in parallel and outputting into two or more All-pass filters in series.
All-Pass filter is a combination of FIR and IIR. Also referred to as a universal filter
  Allows all frequencies through but changes the phase response

## Slide 9: Spatial Effect
Moorer Reverberator
Built on from Schroeder's
Notes: Parallel comb filters with different delay lengths(To Simulate modes of rooms)
All-pass filters which increase reflection density
Low pass filter inserted in feedback loop to alter reverb timing
(a) deals with early reflections of delay and (b) deals with late reflections

## Slide 10: Non-Linear Effect
Overdrive
Distortion
  )
Notes: Intentional non-linear harmonic processing
Overdrive
  Low level driven by High levels in a non-linear curve characteristic
  Schetzen Formula
    Symmetrical soft clipping
Distortion
  Gain controls level of Distortion
  Part of distorted signal is mixed with the original signal for output

## Slide 11: Problems
Simulating ADC
  Demo simulation
  Design file for simulation values
Notes: Started off semester by examining the ADC through an oscilloscope. There was too much data so simulation was the solution. I was able to view the EOC output but the ADC wasn’t outputting a value.
XADC did work on the basys3 with the demo file used but the simulation wouldn’t show an input or output value for the main signal. EOC was
Design file for input values wouldn’t work with the ADC through simulation. Others online had the same problem and solutions suggested did not work.

## Slide 12: Problems
Pmod Interface
  No solution online
  VHDL attempt
Notes: No Verilog solution found online for how to program the Pmod interface

## Slide 13: IIR Results
Notes: Applied a delay of 10 clock cycles
Could apply gains of ½,1/4,1/8 by using an arithmetic shift right of the Data.

## Slide 14: IIR Results
Notes: Applied a delay of 10 clock cycles
Could apply gains of ½,1/4,1/8 by using an arithmetic shift right of the Data.

## Slide 15: FIR Results
Notes: Applied a delay of 10 clock cycles
Could apply gains of ½,1/4,1/8 by using an arithmetic shift right of the Data.

## Slide 16: Overdrive Results
Notes: Applied a delay of 10 clock cycles
Could apply gains of ½,1/4,1/8 by using an arithmetic shift right of the Data.

## Slide 17: Thank You
Questions?